## Slide 1: Introduction to Lego EV3
Summit Denali
https://github.com/vdalal/lego-ev3

## Slide 2: Goal: Demo Day
Goals
Avoid crashes
Stay in the playpen
Move continuously
Learn & have fun!

## Slide 3: Rough Class Schedule & Plan – (1)
Week | Plan | Comments
Week #1 | Introduction - 5 mins EV3 Kit, sensors, code, download etc. Logistics - 5 mins EV3 proficiency, split into groups Norms Discuss - 10 mins Session Goal: Demo Bot MUST work cooperatively (avoid obstacles, not crash) Stay within boundary Discuss/Debate sensor options Build - Driver Base (start) - 45 mins Program - Driver Base Download code Move straight line, move back/forth, & turn Loop(s) Review Goal(s) | 2 students/group, 8 groups, 8 kits Everyone does the same build so we can help each other Challenge: our builds can interact with each other
Week #2 | Discuss: Goal(s) - weekly & session goals Finalize sensor options Program - Driver Base (continued) Move straight line, move back/forth, & turn Loop(s) Add another sensor e.g. ultrasonic sensor Detect obstacle, Stop on obstacle, avoid (turn) on obstacle Add Movement - back/forth & turn Challenge: Display: STOP Sound: Make sound #1 for 3 secs Move back slowly Review Goal(s) | Challenge based on discussion with students
Reference: https://docs.google.com/document/d/1ODXoy8ChpRAfU1ifJo9y75IHdOogI4xekYyTUXGOlkM/edit

## Slide 4: Rough Class Schedule & Plan – (2)
Week | Plan | Comments
Week #3 | Discuss Goal(s) - weekly & session goals Add ONE sensor e.g. light sensor Stay within boundary Stop at line boundary, turn back/around Challenge Kill switch: Touch Sensor Display: END Sound: Make sound #2 for 3 secs Move back slowly Review Goal(s) | Challenge based on discussion with students
Week #4 | Discuss Goal(s) - weekly & session goals Program Challenge Simulate a traffic light Stop & Start Catchup Challenge: Stop at line, turn back/around | Challenge based on discussion with students
Week #5 | Discuss Goal(s) - weekly & session goals Program Demo! Catchup Challenge Stop at line, turn back/around Autonomous driving Review Session Goal(s) Inventory the kits | 
Reference: https://docs.google.com/document/d/1ODXoy8ChpRAfU1ifJo9y75IHdOogI4xekYyTUXGOlkM/edit

## Slide 5: Chrome Web Store

## Slide 6: Launch App

## Slide 7: FAQ
https://le-www-live-s.legocdn.com/sc/media/files/primary/engb%20campaign%20middle%20school%20ev3%20chromebooks%20faqs-80bbd7d15963de5d20a786819aa67ace.pdf?la=en-gb
https://education.lego.com/en-us/support/mindstorms-ev3/software-requirements
  Chromebook
  Operating system:
  Chrome OS version 50 or above
  Hardware:
  4 GB RAM or more
  1.40 GHz dual-core processor or faster
  2 GB available storage space
  Bluetooth 2.0 or above
  Available on Chrome Web Store.
  Firmware update compatibility. To confirm that your Chromebook is able to update the firmware on your EV3 Brick via USB, please open the Chrome web browser in your Chromebook and enter ‘chrome://system’ in the address bar. Locate the version number under ‘uname’. If you have version 3.14 or above, then you should be able to update your EV3 Brick via EV3 Programming. If not, please update your EV3 Brick from the EV3 Lab software.

## Slide 8: Discussion Topics
How does the bot detect another bot?
What sensors shall we use?
What speed should the bot be moving at?
What should occur when your bot detects another bot?
Does can the bot avoid another bot? Does the direction of turn matter?
Should the speed change when it approaches another bot?
How does the bot stay within the playpen? How does your bot detect the red border?
Should the speed change when it detects the border?

## Slide 9: Step #1: Go Straight
Move Tank
Loop (forever)

## Slide 10: Step #2: Go Straight, Move Right
Move Tank
Left/Right Motor Controls

## Slide 11: (optional) Step #2: Go Straight, Turn 180
Move Tank
Left/Right Motor Controls

## Slide 12: Step #3: Object Detection – (1)
Ultrasonic Sensor
Distance Detection
Controls

## Slide 13: Step #3: Switch Block, Object Detection – (2)
Ultrasonic Sensor
Compare
Switch Block
If (condition = ‘Yes’)
Do this
Else
– Do that
Turn right (or 180)
Detect object
<=10 in?
Do nothing

## Slide 14: Milestone #1: Detect & Turn Right (Avoid) - Pseudocode
start
Move
straight
Detect object
<=10 in?
Turn right (or 180)
no
yes

## Slide 15: Milestone #1: Detect Object & Turn Right (Avoid) - Code
Ultrasonic Sensor
If (object within 10 inches)
- Turn right
Else
- Go straight
Turn right (or 180)
Go straight
Detect object
<=10 in?

## Slide 16: Step #4: Red border Detection – (1)
Light Sensor
- Reflected light intensity
Distance Detection
Controls

## Slide 17: Step #4: Red border Detection – (2)
Light Sensor
- Reflected light intensity
If (redline = ‘yes’)
- Turn right
Else
- Go straight
Copyright © Vasu Dalal
Turn right (or 180)
Go straight
Reflected intensity >=60?

## Slide 18: Milestone #2: Detect & Avoid Object + Stay in Playpen
start
Move
straight
Detect object
<=10 in?
Turn right (or 180)
no
yes
Move
straight
Detect red border
?
Turn right (or 180)
yes
no
Option #1

## Slide 19: Milestone #2: Detect & Avoid Object + Stay in Playpen
start
Move
straight
Detect object
<=10 in?
Turn right (or 180)
no
yes
Detect red border
?
yes
Option #2
no

## Slide 20: Milestone #2: Detect & Avoid Object + Stay in Playpen
start
Move
straight
Detect object
<=10 in?
Turn right (or 180)
no
yes
Detect red border
?
yes
Option #3
no

## Slide 21: Milestone #2: Detect Red border & Turn Right - Code
Light Sensor
- Reflected light intensity
If (redline = ‘yes’)
- Turn right
Else
- Go straight
Turn right (or 180)
Go straight
Reflected intensity >=60?

## Slide 22: Milestone #2: Detect Red border & Turn Right - Code
Light Sensor
- Reflected light intensity
If (redline = ‘yes’)
- Turn right
Else
- Go straight
Turn right (or 180)
Go straight
Reflected intensity >=60?

## Slide 23: Goal: Demo Day
Goals
Avoid crashes
Stay in the playpen
Move continuously
Learn & have fun!
Thank you!
https://github.com/vdalal/lego-ev3