## Slide 1: Introduction to Lego EV3
Summit Denali
Vasu Dalal (vdalal@gmail.com)
https://github.com/vdalal/lego-ev3

## Slide 2: Intoductions
Teams: Make your own
  2 students per team, 1 EV3 unit per team
  1 EV3 brick + 1 laptop or ChromeBook
Mentors
  Kritav – 7th grade, Summit Denali
  Pui
  Vasu

## Slide 3: Goal: Demo Day
Goals
Avoid crashes
Stay in the playpen
Move continuously

## Slide 4: Session Goals
Be respectful of each other & the class materials
Participate in class, no other distractions
Explore, Discover & Implement
Collaborate: Help each other, Share with the class
Have fun
Have a personal or team goal – What is that 1 (or 2) thing(s) you want to get from the session?

## Slide 5: Rough Class Schedule & Plan – (1)
Week | Plan | Comments
Week #1 | Introduction - 5 mins EV3 Kit, sensors, code, download etc. Logistics - 5 mins EV3 proficiency, split into groups Norms Discuss - 10 mins Session Goal: Demo Bot MUST work cooperatively (avoid obstacles, not crash) Stay within boundary Discuss/Debate sensor options Build - Driver Base (start) - 45 mins Program - Driver Base Download code Move straight line, move back/forth, & turn Loop(s) Review Goal(s) | 2 students/group, 8 groups, 8 kits Everyone does the same build so we can help each other Challenge: our builds can interact with each other
Week #2 | Discuss: Goal(s) - Session goals Finalize sensor options Program - Driver Base (continued) Move straight line, move back/forth, & turn Loop(s) Add another sensor e.g. ultrasonic sensor Detect obstacle, Stop on obstacle, avoid (turn) on obstacle Add Movement - back/forth & turn Challenge: Display: STOP Sound: Make sound #1 for 3 secs Move back slowly Review Goal(s) | Challenge based on discussion with students
Reference: https://docs.google.com/document/d/1ODXoy8ChpRAfU1ifJo9y75IHdOogI4xekYyTUXGOlkM/edit

## Slide 6: Rough Class Schedule & Plan – (2)
Week | Plan | Comments
Week #3 | Discuss Goal(s) - Session goals Add ONE sensor e.g. light sensor Stay within boundary Stop at line boundary, turn back/around Challenge Kill switch: Touch Sensor Display: END Sound: Make sound #2 for 3 secs Move back slowly Review Goal(s) | Challenge based on discussion with students
Week #4 | Discuss Goal(s) - Session goals Program Challenge Simulate a traffic light Stop & Start Catchup Challenge: Stop at line, turn back/around | Challenge based on discussion with students
Week #5 | Discuss Goal(s) - Session goals Program Demo! Catchup Challenge Stop at line, turn back/around Autonomous driving Review Session Goal(s) Inventory the kits | 
Reference: https://docs.google.com/document/d/1ODXoy8ChpRAfU1ifJo9y75IHdOogI4xekYyTUXGOlkM/edit

## Slide 7: EV3 Brick

## Slide 8: EV3 Elements

## Slide 9: EV3 Buttons

## Slide 10: EV3 Input & Output Ports

## Slide 11: EV3 Motors

## Slide 12: EV3 Color Sensor

## Slide 13: EV3 Sensors & Motors

## Slide 14: EV3 Connection to the laptop (or PC or Chromebook or Mac)

## Slide 15: Build Instructions
Driving Base

## Slide 16: Driving Base
https://education.lego.com/en-us/support/mindstorms-ev3/building-instructions#robot

## Slide 17: Driving Base

## Slide 18: Driving Base – Ultrasonic Sensor

## Slide 19: Driving Base – Color Sensor

## Slide 20: EV3 Programming App

## Slide 21: Green Palette = Action
Green palette = Action blocks eg. sm/med motors, move etc.

## Slide 22: Orange Palette = Logic Control
Orange palette = Logic Flow Control blocks eg. start, loop, switch etc.

## Slide 23: Yellow Palette = Sensor control
Yellow palette = Sensor control blocks eg. Ultrasonic sensor, color sensor, touch sensor etc.

## Slide 24: Debug Environment
Port View, note: ports are connected to one or more sensors

## Slide 25: Download code
Download code
(Q) Why do we need to download code to the EV3 brick?

## Slide 26: Run code
Run code

## Slide 27: Chrome Web Store (chrome.google.com/webstore/)

## Slide 28: Launch App

## Slide 29: FAQ
https://le-www-live-s.legocdn.com/sc/media/files/primary/engb%20campaign%20middle%20school%20ev3%20chromebooks%20faqs-80bbd7d15963de5d20a786819aa67ace.pdf?la=en-gb
https://education.lego.com/en-us/support/mindstorms-ev3/software-requirements
  Chromebook
  Operating system:
  Chrome OS version 50 or above
  Hardware:
  4 GB RAM or more
  1.40 GHz dual-core processor or faster
  2 GB available storage space
  Bluetooth 2.0 or above
  Available on Chrome Web Store.
  Firmware update compatibility. To confirm that your Chromebook is able to update the firmware on your EV3 Brick via USB, please open the Chrome web browser in your Chromebook and enter ‘chrome://system’ in the address bar. Locate the version number under ‘uname’. If you have version 3.14 or above, then you should be able to update your EV3 Brick via EV3 Programming. If not, please update your EV3 Brick from the EV3 Lab software.

## Slide 30: Programming the Bot

## Slide 31: Basics: Action blocks
Large Motor
Steering
Move Tank

## Slide 32: Basics: Logic/Flow Control blocks
Large Motor
Loop
Steering
Switch
condition = true
if (condition)
typically from
a sensor
condition = false

## Slide 33: Basics: Sensor blocks
Large Motor
Loop

## Slide 34: Pseudo Code
Determine what we want to accomplish in English-like language?
e.g.
Go straight forever
  start
  go straight (rotations = 1)
  loop
Go straight forever, turn ‘right’ if object detected
  start
  go straight (rotations = 1)
  if (object detected within 10 inches)
  turn right
  loop

## Slide 35: Pseudo Code – (2)
Determine what we want to accomplish in English-like language
3. Go straight forever, turn ‘right’ if white line (playpen border) detected
  start
  go straight (rotations = 1)
  if (white line detected (reflected intensity or code detection))
  turn right
  loop

## Slide 36: Discussion Topics
Each bot acts on their own. How do the bots coordinate their actions?
How does the bot detect another bot?
What sensors shall we use?
What speed should the bot be moving at?
What should occur when your bot detects another bot?
Does can the bot avoid another bot? Does the direction of turn matter?
How does the bot stay within the playpen? How does your bot detect the red border?
What other improvements can we make? Speed? Finetune turns? etc.

## Slide 37: Framework
Go straight
code
Detect object/
Take Action
Detect
Playpen/ Take Action
Step 1
Step 2
Step 3
Start

## Slide 38: Step #1: Go Straight
Move Tank
Loop (forever)

## Slide 39: Step #2: Go Straight, Move Right
Move Tank
Left/Right Motor Controls

## Slide 40: (optional) Step #2: Go Straight, Turn 180
Move Tank
Left/Right Motor Controls

## Slide 41: Step #3: Object Detection – (1)
Ultrasonic Sensor
Distance Detection
Controls

## Slide 42: Step #3: Switch Block, Object Detection – (2)
Ultrasonic Sensor
Compare
Switch Block
If (condition = ‘Yes’)
Do this
Else
– Do that
Turn right (or 180)
Detect object
<=10 in?
Do nothing

## Slide 43: Milestone #1: Detect & Turn Right (Avoid)
start
Move
straight
Detect object
<=10 in?
Turn right (or 180)
no
yes

## Slide 44: Milestone #1: Detect Object & Turn Right (Avoid) - Code
Ultrasonic Sensor
If (object within 10 inches)
- Turn right
Else
- Go straight
Turn right (or 180)
Go straight
Detect object
<=10 in?

## Slide 45: Step #4: White border Detection – (1)
Light Sensor
- Reflected light intensity
Distance Detection
Controls

## Slide 46: Step #4: White border Detection – (2)
Light Sensor
- Reflected light intensity
If (white border = ‘yes’)
- Turn right
Else
- Go straight
Copyright © Vasu Dalal
Turn right (or 180)
Go straight
Reflected intensity >=60?

## Slide 47: Milestone #2: Detect & Avoid Object + Stay in Playpen
start
Move
straight
Detect object
<=10 in?
Turn right (or 180)
no
yes
Move
straight
Detect white border
?
Turn right (or 180)
yes
no
Option #1

## Slide 48: Milestone #2: Detect & Avoid Object + Stay in Playpen
start
Move
straight
Detect object
<=10 in?
Turn right (or 180)
no
yes
Detect white border
?
yes
Option #2
no

## Slide 49: Milestone #2: Detect & Avoid Object + Stay in Playpen
start
Move
straight
Detect object
<=10 in?
Turn right (or 180)
no
yes
Detect white border
?
yes
Option #3
no

## Slide 50: Milestone #2: Detect & Avoid Object + Stay in Playpen
start
Move
straight
Detect object
<=10 in?
Turn right (or 180)
no
yes
Detect white border
?
Turn right (or 180)
yes
no
Option #4

## Slide 51: Demo Day Program
Object Sensor
If (whiteborder = ‘yes’)
- Turn right
Else
- Go straight
Turn right (or 180)
Go straight
Detect object
<=10 in?
Reflected intensity >=60?
Turn right (or 180)

## Slide 52: Goal: Demo Day
Goals
Avoid crashes
Stay in the playpen
Move continuously
Thank you!
https://github.com/vdalal/lego-ev3